OVERCOMING THE CRISIS OF PLASMA FLOW IN VACUUM ARC IN A STRONG MAGNETIC FIELD

I.A. Krinberg

ISU, Irkutsk, Russia, e-mail: krinberg@physdep.isu.ru

As is known a super-sonic plasma flow is emitted from vacuum arc cathode surface at typical value of 3-5. Here  is the flow velocity,  is the local value of ionic sound,  is the electron temperature, and are the mass and mean charge of ions. In the presence of a strong axial magnetic field the velocity  decreases slowly with a distance  from cathode surface, bur electron temperature increases as [1]. Thus at certain distance  the crisis of plasma flow (i. e. ) occurs if the discharge gap length is larger than . In figure the values of a critical length are given. They have been obtained on the basis of model [1] for conditions of the experimental setup [2]: the external magnetic field is proportional to the arc current as  with =1 mT/A, radius of the cathode (from carbon and titanium) is equal to 3 mm, and  the inter-electrode gap length is 35 mm. As can be seen from figure, the crisis of flow is expected at currents  A.

Crisis would be overcome by means of transition to a non-steady-state motion or to a limiting flow with . Under such assumption the calculations at  have been performed. Mean ion charge values calculated and observed [2], are presented in a figure. Rather close agreement of model calculations and measurements gives evidence of the limiting flow realization in vacuum arc.

###### References

- Krinberg I.A. Appl. Phys. (Russia), 2004, No.6.

- Oks E.M., Anders A., Brown I.G. et al. IEEE Trans. Plasma Sci., 1996, v.24, 1174-1183.

# Text boxes

Ti

C

Ti

C